## Slide 1: 5G, Open Radio, and Vendor Diversity
Andrew Thiessen, Division Chief Institute for Telecommunication Sciences National Telecommunications and Information Administration athiessen@ntia.gov

## Slide 2: Agenda
5G Primer
3rd Generation Partnership Project (3GPP)
Traditional, Virtualized, and Open Radio Access Networks
NTIA’s Efforts in 5G Vendor Diversity

## Slide 3: 5G Primer

## Slide 4: 5G Vision — at the Outset
Gbps bandwidth
10 Mbps/m2 traffic
density
1 million
devices/km2
True ms latency
99,999% reliability

## Slide 5: What spectrum?
7.125GHz
24.25GHz
52.6GHz
410MHz
Frequency
Range 1
Frequency
Range 2
Similar to LTE but with more capacity based on larger channels
Where things are new/different
What are the use cases for each?
Notes: Here I am going to talk about the characteristics of FR1 and FR2 and how they lend themselves to different use cases. And how often this is the first dichotomy that I use to separate out what people mean when they say “5G”

## Slide 6: Architecture
Architecture options for 5G based on acceleration:
Two radio technologies
  LTE
  Next Generation Radio (NR)
Radio level aggregation for both variants
Two core networks
  Evolved Packet Core (EPC – with potential evolutions)
  Next Generation Core Network (NGCN)
This creates 12 options

## Slide 7
EPC
LTE
Option 1) Standalone LTE, EPC connected, Legacy
NGCN
NR
Option 2) Standalone NR, NGCN connected
eNodeB or eNB
gNodeB or gNB
Radio Access Network
(RAN)
User Equipment (UE)
User Equipment (UE)
Evolved Packet Core
Next Generation Core Network

## Slide 8
EPC
LTE
Option 3) Non-Standalone/”LTE assisted”, EPC connected
NGCN
NR
Option 3a) Non-Standalone/”LTE assisted”, EPC connected
EPC
LTE
NGCN
NR
1a

## Slide 9: 5G Non-StandAlone (5G NSA)
Quick deployment of 5G radio
Leverage of existing LTE footprint
Uses LTE radio for all signaling between the UE and the core network
High user throughput
Primarily mid-band spectrum for enhanced mobile broadband

## Slide 10: 5G StandAlone (5G SA)
5G core allows for network functions to be cloud native
Services can be deployed using micro-services to maximize reuse across multiple network functions
New network functions become far easier to deploy
  Time and cost savings
End to end network slicing
  Network slice selection functionality allows for further isolation between slices
Edge computing
  Allows for dynamic traffic management and break out at the edge of the network
  Reduction in latency and increase in reliability
Multiple/different QOS flows within a single packet data stream
Access agnostic by design, with unified registration, authentication, session, mobility and policy management for all access types

## Slide 11
3GPP 5G SA Architecture
AUSF
UDM
AMF
SMF
PCF
AF
UE
RAN
UPF
DN
NG13
NG12
NG8
NG10
NG11
NG7
NG5
NG1
NG15
NR air int
NG3
NG6
NG2
NG4
NG9 – between UPFs
NG14 – between AMFs
Xn

## Slide 12: 3GPP

## Slide 13: What is the 3rd Generation Partnership Project (3GPP)?
The 3rd Generation Partnership Project (3GPP) unites [Seven] telecommunications standard development organizations (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC), known as “Organizational Partners” and provides their members with a stable environment to produce the Reports and Specifications that define 3GPP technologies.
The project covers cellular telecommunications technologies, including radio access, core network and service capabilities, which provide a complete system description for mobile telecommunications.

## Slide 14: 3GPP Original 5G Timeline
Rel-16 Study phase
Q2
Q3
Q4
2019
Q2
Q3
Q4
Q1
2020
Q1
Rel-16 Study and Normative phase
Rel-16 freeze
Rel-16 ASN.1
Rel-15 freeze (incl 5G SA)
Rel-15 late drop freeze
2018
Q1
2017
Q4
Rel-15 NSA (option-3) freeze
Rel-15 NSA (option-3) ASN.1
Rel-15 ASN.1 (incl 5G SA)
Rel-15 late drop ASN.1
“Early drop”
“Main drop”
“Late drop”

## Slide 15: 3GPP Current Timeline
Schedule assumes a return to physical meetings after June 2021

## Slide 16: T/V/O Radio Access Networks

## Slide 17: Break for Terminology (Ugh!)
RAN (Radio Access Network)
O-RAN
Open RAN
oRAN
OpenRAN
ORAN
VRAN
Telecom Infra Project
Disaggregation of hardware from software for RAN
O-RAN Alliance
Open RAN
Virtualized RAN

## Slide 18: Break for Terminology (Ugh!)
RAN (Radio Access Network)
O-RAN
Open RAN
oRAN
OpenRAN
ORAN
VRAN
Telecom Infra Project
Disaggregation of hardware from software for RAN
O-RAN Alliance
Open RAN
Virtualized RAN

## Slide 19: Take a Quick Step Back
EPC
LTE
Option 1) Standalone LTE, EPC connected, Legacy
NGCN
NR
Option 2) Standalone NR, NGCN connected
eNodeB or eNB
gNodeB or gNB
Radio Access Network
(RAN)
User Equipment (UE)
User Equipment (UE)
Evolved Packet Core
Next Generation Core Network

## Slide 20: Traditional Radio Access Network
Remote Radio Head
Proprietary Hardware, Software, and Interfaces

## Slide 21: Virtualized Radio Access Network
Remote Radio Head
Proprietary Hardware and Interfaces
Proprietary Software w/virtualization of functions
Commercial Off The Shelf Hardware

## Slide 22: Open Radio Access Network
Remote Radio Head
General Purpose Processing hardware
Proprietary Software w/virtualization of functions
Commercial Off The Shelf Hardware
Open interface
Let’s not forget open-source code!

## Slide 23: What is NTIA up to around 5G and vendor diversity?

## Slide 24: 5G Testbed
NTIA’s Institute for Telecommunication Sciences is extending its LTE testbed to 5G with a focus on
  Test and evaluation of the integration of open radio access network solutions to determine level of difficulty
  Test and evaluation of the interoperability of open radio access network solutions to determine level of performance with different ORAN builds
  Test and evaluation of virtualized radio access network capabilities and intersection to ORAN
  Integration of NTIA’s Software Bill of Materials (SBOM) goals and objectives based on significant focus of ORAN on open-source capabilities
Can/will coordinate with State Dept to leverage unique capability to work with other laboratories to travel to/from to share knowledge engineer to engineer

## Slide 25: 5G Challenge
NTIA’s Institute for Telecommunication Sciences is partnering with Dept of Defense to explore creation of a challenge to develop open source 5G protocol stacks that support DOD’s mission
Published a Notice of Inquiry in the Federal Register to explore the parameters of the challenge
  https://www.federalregister.gov/documents/2021/01/11/2021-00202/5g-challenge-notice-of-inquiry
Comments close February 10, 2021
Details to search
  5G Challenge
  [Docket No. 210105–0001]
  RIN 0660–XC049

## Slide 26: Wireless Supply Chain Innovation & Multilateral Security
The Public Wireless Supply Chain Innovation Fund to be established and administered by NTIA:
Promote and deploy technology that will enhance competitiveness for 5G based on open and interoperable radio access networks
Accelerate deployment of open interface standards-based radio access network solutions
Promote and deploy compatible equipment between new 5G equipment with future open standards based interoperable networks
Manage integration of multi-vendor network environments
Identify criteria to define equipment as based on open standards for multi-vendor network equipment for interoperability
Promote and deploy security features aimed at enhancing the above
Promote and deploy network function virtualization to facilitate multi-vendor interoperability and a more diverse vendor market

## Slide 27: Vendor Diversity
Challenge: Limited options when selecting vendors to develop and deploy 5G and earlier generation wireless networks
Goal: Unleash the innovative power of the private sector and competition
Opportunity: Lower barriers to entry in the telecommunications equipment market would unlock economic opportunities
Therefore, NTIA is supporting the industry-led development of open, interoperable networks.
Notes: Talking Points:
The U.S. Government recognizes that many network operators face limited options when selecting legacy vendors to develop and deploy 5G and earlier generation wireless networks.
So our goal is to unleash the innovative power of the private sector and competition to develop more secure, robust, resilient, and affordable telecommunications networks for all.
Importantly, lower barriers to entry in the telecommunications equipment market would also unlock economic opportunities for innovative SMEs and entrepreneurs around the world, including in your own countries.
Therefore, like the U.S. Government as a whole, NTIA fully supports industry’s development of open, interoperable telecommunications networks – like those based on open RAN – while also recognizing the importance of maintaining a full suite of solutions offered by incumbent trusted vendors.
This shift to open and interoperable networks would increase competition and provide operators with additional options when purchasing network equipment and services from trusted vendors.

## Slide 28: Vendor Diversity
Promoting the transition toward open and interoperable in a range of multilateral fora, like the Prague 5G Security Conference, OECD, and G7
Engaging directly with foreign governments
Driving U.S. engagement on common international principles on open and interoperable network architectures
Contributing to activities like USTTI and other relevant efforts
We want to hear from you!
Notes: While efforts to increase vendor diversity should be industry-led, governments also have a role to play in fostering enabling environments for innovative approaches like open RAN.
Therefore, NTIA is working in collaboration with interagency partners to support efforts by companies around the world to develop open and interoperable telecommunications networks.
To that end, we have actively highlighted the importance of vendor diversity in multilateral fora like the 2020 Prague 5G Security Conference and the OECD, and we look forward to continuing those discussions during this year’s G7 cycle.
We’re also speaking one-on-one with foreign governments to explain, discuss, and potentially coordinate on open RAN and other vendor diversity-related matters. We hope that this presentation can be the start of that discussion with your own governments.
We also see an opportunity to build on the Prague Proposals by working with industry and international partners to develop principles on what governments can do to promote open and interoperable networks.
And finally, we are participating in worthwhile capacity-building activities like USTTI to further raise awareness of these issues.
As I mentioned, we would like to begin a dialogue with all of you on this important topic, so I hope that after this training you will feel free to reach out to our International Affairs team to learn more.
Thank you.